## Slide 1
Magnetic Resonance Imaging:
Basic Introduction
Louvain-la-Neuve - Neuroimaging Workshop 2019
Jorge Jovicich
Center for Mind/Brain Sciences (CIMeC),
University of Trento, Rovereto, Italy
CIMeC: https://www.cimec.unitn.it/
MRI Methods Group: http://r.unitn.it/en/cimec/mri
E-mail: jorge.jovicich@unitn.it

## Slide 2
Center for Mind/Brain Sciences, University of Trento, Italy
MRI Methods Group: http://r.unitn.it/en/cimec/mri
Focus on: Quantification of brain plasticity
  General: Develop & apply novel MRI techniques to quantify brain plasticity
  Specific: Optimize accuracy, reproducibility and sensitivity of brain plasticity metrics derived from anatomical, diffusion and functional MRI.
Anatomical
Diffusion
rsfMRI
MRI Tools
Applications
Healthy
Blind
Deaf
Dementia
Psychosis
Schizophrenia
Surgery
Proton therapy
Developments
Contrast optimization
Distortion correction
Reproducibility
Multicentric harmonization
Ex-vivo validations
1.5T, 3T, 7T, 9.4T
3T Prisma Siemens, CIMeC
Through collaborations
Introduction

## Slide 3
MR Image & Contrast
NMR Signal origin
Spatial encoding
Magnetic gradients
Pulse sequences
Powerful magnet
Radio frequency
Magnetic field gradients
MR Safety
Powerful magnet
Radio frequency
Magnetic field gradients
Structural MRI
Functional MRI
Diffusion MRI
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Pre-processing
Lecture 1
Lecture 2
Lecture 3
Lecture 4
Concept map for lectures
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 4
What is the source of the NMR signal?
How do we measure it?
How do we make images from it?
NMR: Nuclear Magnetic Resonance
Lecture 1 outline
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 5
The «magic» of MRI
One non-invasive
instrument
Pulse
Sequences
Analyses
Models
Etc.
Quantification of multiple
tissue and physiology properties
Quantum mechanics
Where do foundations come from?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 6
Pendulum analogy

## Slide 7
When considering typical experiments with biologic tissue
Water molecules (H2O)
The proton has a spin
(little magnet)
w: Larmor frequency
: giromagnetic ratio (42.58 MHz/T)
B: local magnetic field
have hydrogen atoms,
each with a proton
Proton follows
external magnetic field
Angular rotation: w =  B
What is the source of an NMR signal?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 8
1) Create an equilibrium magnetization (M0)
Put subject in a strong static magnetic field (e.g., 3T)
2) Excite the magnetization away from equilibrium
Transmit radio waves into subject [2~10 ms, mT]
3) Measure the signal induced as the magnetization relaxes to equilibrium
B0
M0
time
Equilibrium
RF
Equilibrium
NMR
signal
B0
B0
B0
B0
M0
M(t)
M(t)
M(t)
Jorge Jovicich,
1
2
3
1
How do we obtain an NMR signal?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 9
1 Tesla = 20,000x Earth’s magnetic field
Magnetic field
from a
coil & current
Magnetic field
from a
bar magnet
Need for a strong and uniform magnetic field
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 10
B0 = constant magnetic field
(always on!)
Along z-axis
Superconducting coil
For fMRI
1.5T, 3T, 4T,
7T, and above…
Z
Where is the magnetic field in the MRI scanner?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 11
Cross section of winding from a superconductive magnet with NbTi multifiliments embedded in a Cu core
http://mriquestions.com/superconductive-design.html
http://www.sprawls.org/mripmt/MRI02
https://www.slideshare.net/padmanishailesh/mri-hardware
How do we generate a static magnetic field?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 12
NMR Signal
  Equilibrium magnetization (Mo)
  Excitation of Mo away from equilibrium
  Relaxation of Mo to equilibrium
Quick review
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 13
: uniform static magnetic field
: static macroscopic magnetization
: Larmor frequency
Bo
Mo
Mo
Net Equilibrium magnetization M0:
- Mz aligned always with B0
- Mxy = 0
- M0 is the vectorial sum of millions of small magnetizations from the protons, which are all rotating at the same Larmor frequency, but out of phase
z
Bo
x
y
Sample in static magnetic field:
equilibrium magnetization
Jorge Jovicich
CIMeC, University of Trento, Italy
0

## Slide 14
NMR Signal
  Equilibrium magnetization (Mo)
  Excitation of Mo away from equilibrium
  Relaxation of Mo to equilibrium
Quick review
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 15
Magnetization excitation: radio frequency (RF) pulse at Larmor frequency
Need a resonant driving force
Like pushing a child on a swing
Child will absorb energy only if
transmitted at the right frequency
Magnetization excitation needs resonance
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 16
Source: Brian Hargreaves (mrsrl.stanford.edu/~brian/mri-movies/ )
Excitation of the magnetization with an
external RF field
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 17
Equilibrium magnetization
in B0 magnetic field
What happens immediately after a RF pulse?
Jorge Jovicich
CIMeC, University of Trento, Italy
x
y
z
Mxy
Mz
M: magnetization rotated by RF pulse
Mz = M0 cos(α), longitudinal magnetization
Mxy = M0 sin(α), transverse magnetization
α
M
x
y
z
RF excitation
flip angle α
M0
M0: magnetization at equilibrium
Magnetization after absorbing the RF
energy and rotating a fling angle 
RF

## Slide 18
NMR Signal
  Equilibrium magnetization (Mo)
  Excitation of Mo away from equilibrium
  Relaxation of Mo to equilibrium
Quick review
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 19
Source: Brian Hargreaves (mrsrl.stanford.edu/~brian/mri-movies/ )
Magnetization Mxy
Transverse component
Magnetization Mz
Longitudinal component
Transverse and longitudinal
magnetization relaxation to equilibrium
Jorge Jovicich
CIMeC, University of Trento, Italy
x
y
z
Mxy
Mz
α
M
Decay of Mxy to equilibrium
Exponential
T2: Charateristic decay time
Recovery of Mz to equilibrium
Exponential
T1: Charateristic recovery time

## Slide 20
What is the T1 relaxation?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 21
90° pulse
After the RF, each proton spin has a slightly different 0=B0
Some go slower, some faster  they come out of phase
Net transverse magnetization Mxy decays to zero (equilibrium)
What is the T2 relaxation?
Jorge Jovicich
CIMeC, University of Trento, Italy
T2 relaxation
Equilibrium
Immediately after RF pulse
After RF pulse

## Slide 22
Loss of phase coherence
Mxy(t)
What is happening during T2 relaxation?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 23
RF
time
Mxy
(Signal)
time
o

Spectra
(Fourier Transform
of time signal)
wo =  Bo
Where is the NMR signal coming from?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 24
Transmits RF excitation pulse
Receives RF induction signal
The radiofrequency (RF) coil
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 25
RF
Voltage
(Signal)
time
Mz
Mxy
time
time
time
x
y
z
Mxy
Mz
M: magnetization rotated by RF pulse
Mz = M cos(α), longitudinal magnetization
Mxy = M sin(α), transverse magnetization
α
RF excitation
flip angle α
Mz: exponential recovery
(relaxation time T1)
Mxy: exponential decay
(relaxation times T2, T2*)
wo =  Bo
Relaxation of magnetization to equilibrium
Jorge Jovicich
CIMeC, University of Trento, Italy
time
time
time
time
M

## Slide 26
From Mike Moseley
T1 and T2 reflect the local tissue environment
Why are relaxation times so important?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 27
From Mike Moseley
T1 relaxation
  Related to water rotational times
  Free protons (cerebral spinal fluid) -> long T1 relaxation
  Bound protons (myelin water) -> short T1 relaxation
What do relaxation times actually mean?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 28
From Mike Moseley
T1 relaxation
  Related to water rotational times
  Free protons (cerebral spinal fluid) -> long T1 relaxation
  Bound protons (myelin water) -> short T1 relaxation
T2 relaxation
  Related to water translational (diffusion) times
  Free protons (cerebral spinal fluid) -> long T2 relaxation
  Bound protons (myelin water) -> short T2 relaxation
What do relaxation times actually mean?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 29
From Mike Moseley
Brain tissue
  Bound protons
  Short T1 relaxation
  Short T2 relaxation
Cerebral Spinal Fluid (CSF)
  Free protons
  Long T1 relaxation
  Long T2 relaxation
What do relaxation times actually mean?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 30
Voltage
(Signal)
time
Mxy
Real signal decays faster than T2 predictions
Pure T2: random spin-spin interactions with perfect
homogeneous external B0
In reality: Field is inhomogeneous (Breal = B0 + B)
Signal decay due to random and fixed dephasing effects: T2*
wo =  Bo
An imperfect world: T2* decay
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 31
The brain that is close to the frontal
sinues will be challenging for fMRI
Where in the head is T2* short?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 32
Mathematical Description: precession + relaxation (Bloch equations)
B0
M0
time
Equilibrium
RF
Equilibrium
NMR
signal
Geometrical description: damped precession
B0
B0
B0
B0
M0
M(t)
M(t)
M(t)
Magnetization dynamics
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 33
NMR Signal
  Equilibrium magnetization (Mo)
  Excitation of Mo away from equilibrium
  Relaxation of Mo to equilibrium
Quick review
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 34
What is the source of the NMR signal?
  The equilibrium magnetization when sample is at B0
  The magnetization comes from protons, mostly in H2O
  Precession frequency at equilibrium: 0 =  B0
What do we need to measure an NMR signal?
  Excitation pulse (B1), must be on resonance ( to B0)
  Magnetization rotated away from equilibrium (flip angle)
What are T1, T2 and T2* relaxation?
  T1: Longitudinal magnetization recovery to equilibrium
  T2: Transverse magnetization recovery to equilibrium (zero) considering only
  proton-proton magnetic field interactions
  T2*: like T2, but adding contributions from static magnetic field inhomogeneities
  T1, T2 and T2* depend on local tissue environments
Summary of concepts introduced
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 35
B0
M0
time
Equilibrium
RF
Equilibrium
NMR
signal
B0
B0
B0
B0
M0
M(t)
M(t)
M(t)
From the whole sample
No spatial selectivity
How can we put spatial information in the signal?
So far no image…
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 36
After the RF excitation, in a uniform static magnetic field B0, the NMR signal:
  Comes from the whole sample: no spatial information
  It decays exponentially with T2*
  It oscillates at wo
time
If I could vary net magnetic field in space (B=B0 + something)
  Then the measured frequency will change following the same law
  Then frequency and space will be related
  Then measuring frequencies tells us where the signal comes from
  We are encoding spatial information in the signal
Spatial encoding concepts
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 37
I know
these
If I can
measure
this
Then:
linear magnetic
field gradient
I can
calculate
this
WHY?? To modulate the resonance frequency as function of space
WHY?? To measure frequencies and know where they come from
Spatial encoding with a magnetic field gradient
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 38
Effect of a magnet gradient
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 39
Magnetic gradients: phase and frequency
Jorge Jovicich
CIMeC, University of Trento, Italy
Gradient along x-axis
Two spatial-encoding possibilities for the magnetization:
Phase changes along x-axis
Frequency changes along x-axix

## Slide 40
A linear gradient is turned on
Let’s look spins in the blue and red position
Source: http://mrsrl.stanford.edu/~brian/mri-movies
Effect of a magnet gradient
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 41
Key points so far:
  Magnetic field gradients encode spatial information in the frequency of the NMR signal:
  So: the spatial information is in the signal frequency
  But: the NMR signal measured is a signal that changes in time
  So: To get spatial information we need to transform temporal information into frequency information
    We need a Fourier Transform ‘massage’
    to transform the measured signal (time)
    into an image (signal of frequency)
Spatial encoding concepts
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 42
https://www.youtube.com/watch?v=cZgl7rJKs3A
Decomposing complex signals in simple waves
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 43
What is the Fourier Transform of a signal?
Signal Intensity as
function of time
time
w
w1
w2
Signal Intensity as
function of frequency
Fourier
Transform
Signal as function of time
Signal as function of frequency
Joseph Fourier (1768-1830)
Equivalent
descriptions!
The Fourier transform
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 44
A
w
w0
3w0
Frequency space of signal S3
Fourier Transform: strength of signal at each frequency
Fourier transform concepts
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 45
Images: http://www.magnet.fsu.edu/education/tutorials/magnetacademy/mri/page5.html
Magnetic field gradients in 3 dimensions
Jorge Jovicich
CIMeC, University of Trento, Italy
Need three orthogonal
magnetic gradients
Slice selection
Phase encoding
Frequency encoding

## Slide 46
Magnetic field
Tissue protons align
with magnetic field
(equilibrium state)
RF pulses
Protons absorb
RF energy
(excited state)
Relaxation
processes
Protons emit RF energy
(return to equilibrium state)
NMR signal
detection
Relaxation
processes
Spatial encoding
using magnetic
field gradients
Subject
Safety screening
RAW DATA
MATRIX
Fourier transform
IMAGE
S(t1,t2)
S(x1,x2)
Larmor Equation
Overview of an MRI procedure
Jorge Jovicich
CIMeC, University of Trento, Italy
Repeat

## Slide 47
The signal we measure is in
spatial frequency space (k-space)
A sequence of RF and gradient pulses which gives NMR signals
What is an NMR or MRI pulse sequence?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 48
What we actually measure
Fourier
Transform
What we want
Data in: K-space
(“signal space”)
Same data in image space
(frequency of signals)
The spatial information is in the frequency of the measured signal
Why are we talking about this?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 49
Understanding k-space
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 50
Understanding k-space
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 51
Understanding k-space
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 52
NMR experiment combining these three gradients:
Select a slice (RF excitation + Gslice)
Select a row (signal acquisition + Gread)
Select a column (Gphase before signal)
B0
M0
time
Equilibrium
RF
Equilibrium
NMR
signal
acquisition
B0
B0
B0
B0
M0
M(t)
M(t)
M(t)
For the
NMR
signal:
For spatial
encoding of
the NMR signal:
Gslice
Gphase
Gread
RF
excitation
What is needed to obtain an MRI?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 53
What is the source of the NMR signal?
What do we need to measure an NMR signal?
What are T1, T2 and T2* relaxation?
How is spatial information encoded in the NMR?
What is a pulse sequence?
Summary of concepts introduced
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 54
Static magnet (always on)
(1.5T , 3T, 7T– 11.7 T)
Earth 10-5 T
Projectiles
MRI Risks & Safety
https://www.dailymotion.com/video/x2y23p7
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 55
Static magnet (always on)
(1.5T , 3T, 7T– 11.7 T)
Earth 10-5 T
Projectiles
RF Coil
(8-64 channels)
Heating
Magnetic gradient coil
(40-100 mT/m
100 A in 100 s)
Peripheral nerve stimulation
Acoustic noise
MRI Risks & Safety
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 56
Structural
MPRAGE
Structural
Diffusion
Functional
EPI
Acoustic stimulation during MRI
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 57
Risks and safety procedures are known
Unfortunately, accidents still happen
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 58
MRI studies are safe if proper precautions are taken
Summary of precautions
  Annual safety training review (MRI lab staff and users)
  Always be aware of the potential dangers of MRI
  Never take anything metal into the scan room
  Always make safety a top priority while in the MRI environment
More information about MRI safety issues:
  http://www.mrisafety.com/
  http://www.radiology.upmc.edu/MRsafety/
MRI Risks & Safety
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 59
General MRI information sites include:
http://www.cis.rit.edu/htbooks/mri
http://mriquestions.com/
http://www.fmri4newbies.com/
https://www.imaios.com/en/e-Courses/e-MRI
Other:
http://matt.might.net/articles/ways-to-fail-a-phd/
https://gate.nmr.mgh.harvard.edu/wiki/whynhow/
MRI educational links include:
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 60
MR Image & Contrast
NMR Signal origin
Spatial encoding
Magnetic gradients
Pulse sequences
Powerful magnet
Radio frequency
Magnetic field gradients
MR Safety
Powerful magnet
Radio frequency
Magnetic field gradients
Structural MRI
Functional MRI
Diffusion MRI
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Pre-processing
Lecture 1
Lecture 2
Lecture 3
Lecture 4
Concept map for lectures
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 61
Atoms (“indivisible” in Greek, Democritus 460-370 BC )
Atomic theory & experiments: hydrogen (Cavendish, 1766)
Atomic nuclei, proton (Rutherford, 1911)
Quantum theory (Planck, Einstein, Bohr, etc. starts early 1900)
Atomic nuclei: spin (Pauli, 1924)
Atomic nuclei in a gas can absorb energy in a magnetic field (Rabi, 1937)
  Nuclear Magnetic Resonance (NMR)
NMR possible also in solid & liquids (Purcell & Bloch, 1945)
Magnetic gradients proposed to create MRI (Lauterbur & Mansfield, 1972)
Historical perspective
Isidor Isaac Rabi
Nobel Price 1944
Edward Purcell & Felix Bloch
Nobel Price 1952
What is the source of an NMR signal?
P. Lauterbur & P. Mansfield
Nobel Price 2003
Jorge Jovicich
CIMeC, University of Trento, Italy