## Slide 1
Brain Diffusion MRI Introduction
Louvain-la-Neuve - Neuroimaging Workshop 2019
Jorge Jovicich
Center for Mind/Brain Sciences (CIMeC),
University of Trento, Rovereto, Italy
CIMeC: https://www.cimec.unitn.it/
MRI Lab: http://r.unitn.it/en/cimec/mri
E-mail: jorge.jovicich@unitn.it

## Slide 2
MR Image & Contrast
NMR Signal origin
Spatial encoding
Magnetic gradients
Pulse sequences
Powerful magnet
Radio frequency
Magnetic field gradients
MR Safety
Powerful magnet
Radio frequency
Magnetic field gradients
Structural MRI
Functional MRI
Diffusion MRI
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Pre-processing
Lecture 1
Lecture 2
Lecture 3
Lecture 4
Concept map for lectures
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 3
Lecture 3 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain diffusion:
Why do we care?
How do we measure it?
How do we pre-process data?
Extracting information: models & challenges

## Slide 4
1.5cm x 1.8cm,
8.5um x 8.5um
Courtesy of Hui Wang
Fibre diameters in human brains ranged from 0.16 to 9 μm
Liewald et al. 2014
Brain anatomy characterization (in-vivo, non-invasive)
  Brain tissue microstructure (axon diameter, density, myelination, etc.)
  White matter fibers (orientations, connections, etc.)
Diffusion of water molecules in tissue
  Reflects the local microstructural environment
  Physical restrictions will affect diffusion magnitude and directionality
Diffusion MRI
  Contrast sensitive magnitude and direction of water diffusion
  Models relate the NMR signal with microstructure properties
Courtesy of Viviana Siless & Chiara Maffei
Diffusion MRI: Motivation
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 5
Why bother about molecular diffusion in brain?
Water molecules diffuse differently inside biological tissues
We can differentiate brain tissues based on different diffusion profiles within them
White matter: anisotropic
Gray matter: isotropic
Courtesy of Viviana Siless & Chiara Maffei
Water diffusion in the brain
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 6
Lecture 3 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain diffusion:
Why do we care?
How do we measure it?
How do we pre-process data?
Extracting information: models & challenges

## Slide 7
90°
180°
Modified from Viviana Siless & Chiara Maffei
So
what?
?
Diffusion MRI overview
Jorge Jovicich
CIMeC, University of Trento, Italy
microstructure
connectivity

## Slide 8
Diffusion contrast: based on gradients
Jorge Jovicich
CIMeC, University of Trento, Italy
Gradient along x-axis
Two spatial-encoding possibilities for the magnetization:
Phase changes along x-axis
Frequency changes along x-axix
REMINDER

## Slide 9
gy
gy
90°
180°
δ
Δ
echo
G
Pulse Gradient Spin Echo sequence (PGSE)
Gy Gradient
y
x
Courtesy of Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: how do we measure it?

## Slide 10
Diffusion in the x direction
gy
gy
90°
180°
δ
Δ
echo
G
→ No displacement along y-axis
→ No dephasing induced by y-gradient
→ No MR signal attenuation cause by diffusion y-gradient
y
x
Pulse Gradient Spin Echo sequence (PGSE)
Courtesy of Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: how do we measure it?

## Slide 11
gx
gx
90°
180°
δ
Δ
echo
G
Pulse Gradient Spin Echo sequence (PGSE)
y
x
Courtesy of Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: how do we measure it?

## Slide 12
gx
gx
90°
180°
δ
Δ
echo
G
→ Displacement captured by the diffusion x-gradient
→ Dephasing of magnetization
→ Signal attenuation caused by diffusion gradients
Diffusion in the x direction
Pulse Gradient Spin Echo sequence (PGSE)
y
x
Courtesy of Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: how do we measure it?

## Slide 13
B0 : baseline image
g1 g2 g3 g4 g5 g6
Many possible configurations can appear in each voxel: In one mm cubic voxel there are millions of axons of ~um resolution.
Because of the orientation dependency in encoding diffusion, multiple diffusion directions (b-vector) are needed to cover the full 3D profile.
Diffusion weighted images (DWI)
Multiple
gradient
encoding
directions
Sensitivity to diffusion in multiple directions
Courtesy of Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: how do we measure it?
Notes: Fully isotropical distributed directions are optimal. More directions are better than more averages for scan time. Trade off between bval and dw directions. The range of bval and bvecs sampled is called the q space

## Slide 14
Baseline: B0
g1
Diffusion encoding:
Only along the specific direction applied
Image intensity is attenuated depending on water diffusion for the specific direction.
We compare each image direction to a baseline image (no direction, B0).
g2
Low
dMRI
signal
High
dMRI
signal
Courtesy of Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: how do we measure it?
Notes: No diffusion, the spins experience the same gradient encoding, they rewind, there is no dephase.

## Slide 15
MRI signal:
b-value (diffusion weight): Measure of diffusion sensitivity
Large b → strong diffusion sensitivity
The b-value depends on the sequence and acquisition parameters:
δ
Δ
G
90°
180°
Pulse Gradient Spin Echo sequence (PGSE)
Ɣ → gyromagnetic ratio
G → diffusion gradient strength
δ → duration of the diffusion-encoding pulse
Δ → the interval between diffusion pulses
b = ɣ2 G2 δ2 (Δ - δ/3)
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: what is the b-value?
S(b) = S0 e-bD
Kim & Kim 2016

## Slide 16
b-value increase  increased contrast between areas of higher and lower diffusivity
  Higher diffusion sensitivity
  Longer diffusion time
Increasing the length of the diffusion-encoding gradient pulses
→ Increased echo time (TE) → Decreased signal-to-noise-ratio (SNR)!
To scan with high b-value you need STRONG and FAST magnetic gradients ($$)
G
Δ
δ
Clinical MRI scanners → Gmax = 40 mT/m
Prisma scanner → Gmax = 80 mT/m (MGH)
HCP scanners → Gmax = 300 mT/m (MGH)
Some animal scanners → Gmax = 1000 mT/m
Gmax | Desired b | Needed δ | Resulting TE
40 mT/m | 1000 s/mm2 | 24 ms | 48 ms
1000 mT/m | 1000 s/mm2 | 3 ms | 6 ms
δ
Δ
G
Modified from Viviana Siless & Chiara Maffei
TE
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: why is the b-value important?
Notes: Add prisma

## Slide 17
b-value increase  increased contrast between areas of higher and lower diffusivity
  Higher diffusion sensitivity
  Longer diffusion time
Increasing the length of the diffusion-encoding gradient pulses
→ Increased echo time (TE) → Decreased signal-to-noise-ratio (SNR)!
To scan with high b-value you need STRONG and FAST magnetic gradients ($$)
G
Δ
δ
δ
Δ
G
TE
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: why is the b-value important?
Notes: Add prisma

## Slide 18
B0 baseline image
In a voxel
  many possible orientations for molecular diffusion
  many different levels of diffusion
Ideally you want to acquire diffusion MRI data with
  Different b-values (sensitivity to different ranges of diffusion)
  Multiple gradient-encoding directions for each b-value (sensitivity in 3D space)
b1
b2
g1b1 g2b1 g3b1 g4b2 g5b2 g6b2
Modified from Viviana Siless & Chiara Maffei
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: b-value and gradient directions
Derek Jones, 2010
Notes: Fully isotropical distributed directions are optimal. More directions are better than more averages for scan time. Trade off between bval and dw directions. The range of bval and bvecs sampled is called the q space

## Slide 19
b0
b0
b0
b0
...
DWI
DWI
Diffusion MRI
acquisition
Schemes
(single/multishell)
b0
b0
...
DWI
DWI
b0
...
DWI
DWI
...
b0 interleaved
b0 at start
(some scanners average b0s)
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI data structure
Multiple 3D brain volumes, each one with fast-MRI (spin-echo Echo Planar Imaging)
Several of them are b0 (used for diffusion estimation and for head motion correction)
Several diffusion weighted images:
  Single-shell: means there is one b-value for diffusion encoding,
  multiple gradient encoding directions
  Multi-shell: mean there are many different shells
Your pulse sequence defines the order in which b-values and directions are acquired

## Slide 20
Lecture 3 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain diffusion:
Why do we care?
How do we measure it?
How do we pre-process data?
Extracting information: models & challenges

## Slide 21
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI pre-processing

## Slide 22
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI pre-processing

## Slide 23
Marker helps
Check right/left
dicom2nii
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: reformatting

## Slide 24
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI pre-processing

## Slide 25
Thermal noise sources
  Detection system: random electron motion in electronic
  Sample: random spin fluctuations
Noise in diffusion MR signal
  Will propagate through analysis & modelling
  Will affect accuracy and reproducibility
  Need to optimize SNR with acquisition parameter choices
Post processing noise reduction
  Smoothing
    Blurs image, spatial resolution loss
  Total generalized variation regularization
    Preserve edges
    Regularization parameter dependent
  Principal component analysis
    Uses data redundancy
    Preserves accuracy and spatial resolution
    Identifyes + eliminates noise-only components
Manjon et al. Med. Image Anal.c 2008
Rudin et al. D: Nonlinear Phenomena, 1992
Hotelling, J. Educ. Psychol., 1933
Veraart et al. NeuroImage, 2016
    RAW
    ANLM
    TGV
    MPPCA
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Signal denoising

## Slide 26
Raw data
3T Siemens Prisma example (1.8mm isotropic, TE=72ms, TR=5.2s)
  number of b0: 5 (1 at the beginning, 4 at the end)
  number of directions per each shell: 64
  b-values (>0): 500, 1500, 3000 s/mm2 (17 min acquisition)
MPPCA denoised data
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Signal denoising

## Slide 27
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI pre-processing

## Slide 28
What is Gibbs ringing?
  Every signal can be decomposed by an infinite Fourier series
  A truncated series gives an imperfect signal representation
  At signal «edges» this effect is seen as artificial signal ringing fluctuations
125 harmonics
5 harmonics
Step function representation
https://en.wikipedia.org/wiki/Gibbs_phenomenon
CSF
Corpus
Callosum
CSF
Corpus
Callosum
Veraart et al. MRM, 2016
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Gibbs ringing

## Slide 29
Correction: reinterpolate the image based on local, subvoxel-shifts to sample the ringing pattern at the zero-crossings of the oscillating sinc-function (Kellner et al., MRM 2016)
[Full k-space acquisition assumption]
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Gibbs ringing correction

## Slide 30
Effects on FA
MRITrix course
Uncorrected
Corrected
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Gibbs ringing correction

## Slide 31
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
SE-EPI
AP/PA
Geometric
Distortion
correction
Bias field correction
Field map
3D T2
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI pre-processing

## Slide 32
B0 field map
(coronal image) 1.5T
Bo
Air
Water
Phantom images courtesy of Larry Wald
Image reconstruction assumes uniform B0 in the sample
True field is different:
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: susceptibility distortions

## Slide 33
Image reconstruction assumes uniform B0 in the sample
True field is different:
As a result, fast diffusion images (Echo Planar Images, EPI) show:
    areas with signal loss (where T2*<<TE): nothing to do!
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: susceptibility distortions

## Slide 34
Image reconstruction assumes uniform B0 in the sample
True field is different:
As a result, fast diffusion images (Echo Planar Images, EPI) show:
    areas with signal loss (where T2*<<TE): nothing to do!
    areas with geometric distortions: something to do!
x, y : voxel shifts in x, y directions in mm
: proton gyromagnetic ratio
FOVx, FOVy : field of view in x, y direction in mm
tx, ty : sampling interval in x, y direction ( 1/sampling rate)
Voxel shifts relative to true voxel location:
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: susceptibility distortions

## Slide 35
Tournier et al., MRM 2011
Diffusion data overlaid on T1 anatomical
Data are not aligned due to uncorrected distortions
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: susceptibility distortions

## Slide 36
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
SE-EPI
AP/PA
Geometric
Distortion
correction
Bias field correction
Field map
3D T2
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI pre-processing

## Slide 37
b0
b0
b0
b0
...
DWI
DWI
Diffusion MRI
acquisition
Schemes
(single/multishell)
b0
b0
...
DWI
DWI
b0
...
DWI
DWI
...
b0 interleaved
b0 at start
(some scanners average b0s)
Veraart, ISMRM 2019
You wish!
In reality
spins experience
another induced
gradient
Assumed gradient waveform
Effective gradient waveform
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Eddy and motion correction

## Slide 38
http://mriquestions.com/eddy-current-problems.html
Induction kitchen principle
Jorge Jovicich
CIMeC, University of Trento, Italy
Sometimes Eddy currents are welcome

## Slide 39
Le Bihan et al., Artifacts and pitfalls in diffusion MRI, JMRI 2006
Pierpaoli, ISMRM Diffusion, 2016
Eddy currents: strongest effects in phase-encoding direction
Electrical currents in induced inside the MRI cryostat
They generate a magnetic field gradient that adds to the intended one
The net gradient is incorrect leading to image geometric distortions
b0
DWI
DWI
DWI
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Eddy current distortions

## Slide 40
Bastiani et al., Neuroimage 2019
Minimizing head motion:
Subject preparation
Subject fixation
Acquisition as short as needed
Prospective correction
Retrospective correction
  Spatial model Eddy fields
  Optimized registrations
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: head motion

## Slide 41
Bastiani et al., Neuroimage 2019
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: head motion & Eddy currents

## Slide 42
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/eddy
Before any correction | After correction for: eddy currents, gross subject movement, static susceptibility map | After correction for: eddy currents, gross subject movement dynamic susceptibility map
Andersson et al., Neuroimage 2018
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: head motion & Eddy currents

## Slide 43
Raw data
3T Siemens Prisma example:
  number of b0: 5 (1 at the beginning, 4 at the end)
  number of directions per each shell: 64
  b-values (>0): 500, 1500, 3000 s/mm2.
Eddy current correction
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: head motion & Eddy currents

## Slide 44
Tournier et al., MRM 2011
Pierpaoli, ISMRM Diffusion, 2016
Uncorrected
corrected
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: head motion & Eddy currents

## Slide 45
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
SE-EPI
AP/PA
Geometric
Distortion
correction
Bias field correction
Field map
3D T2
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: pre-processing

## Slide 46
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: pre-processing

## Slide 47
Imperfect B1 modulation
  Intensity modulation
Evaluate with image intensity windowing
Correction strategies
  Estimate B1 map on b0
  Apply correction to all dMRI data
  ANTs N4 (no priors) fits smooth bias field that maximizes frequency
Tustison et al., IEEE Trans Med Imag 2010
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Bias field correction

## Slide 48
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
Sample preparation
This is a generic example
Jury out for optimal details
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: pre-processing

## Slide 49
Visual inspection
  Informative but time consuming
  Look at summary metrics
    Standard deviation map across DWI (Eddy currents)
    Standard deviatin across b0 (cardiac pulsation)
    Diffusion tensor residual map
Tournier et al., MRM 2011
Bed vibrations
Insufficient fat suppression
RF spike/interference
Diffusion MRI: Quality check

## Slide 50
Visual inspection
  Informative but time consuming
  Look at summary metrics
    Standard deviation map across DWI (Eddy currents)
    Standard deviatin across b0 (cardiac pulsation)
    Diffusion tensor residual map
    ...
Automated quality tools
  TORTOISE (https://www.nitrc.org/projects/tortoise)
  DTIprep (https://www.nitrc.org/projects/dtiprep)
  DTI Studio (http://dsi-studio.labsolver.org)
  SQUAD – FSL (https://git.fmrib.ox.ac.uk/matteob/eddy_qc_release.git)
  ...
Tournier et al., MRM 2011
Bed vibrations
Insufficient fat suppression
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Quality check

## Slide 51
  SQUAD – FSL (https://git.fmrib.ox.ac.uk/matteob/eddy_qc_release.git)
Bastiani et al., Neuroimage 2019
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Quality check

## Slide 52
  SQUAD – FSL (https://git.fmrib.ox.ac.uk/matteob/eddy_qc_release.git)
Bastiani et al., Neuroimage 2019
Gaussian process model used to replace an motion outlier volume with a new one
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Quality check

## Slide 53
dMRI
dicom
dMRI nii
bval.txt
bvec.txt
Signal Denoise
Gibbs ringing
correction
Eddy & motion correction
Geometric
Distortion
correction
Bias field correction
Quality
check
Signal
model
etc.
b-vector
reorientation
Various pre-processing tools available:
https://tortoise.nibib.nih.gov
https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FDT
https://www.mrtrix.org
...
This is a generic example
Jury out for optimal details
Sample preparation
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: pre-processing

## Slide 54
Diffusion sensitivity (modelling)
  High b-value, multiple b-values (SNR)
  High # directions per b-value (acq time)
Maximize speed:
  Single-shot EPI (multishot challenges)
  Shortest volume TR (> 5. T1 relevant tissue)
  Simultaneous multislice (shortens TR, no SNR costs)
  Multichannel coils (enables SMS)
  Parallel imaging (accelerates with SNR costs, distortions)
  Fast and strong magnetic gradients ($, PNS)
Maximize SNR
  Shortest TE possible (attention w. acceleration)
  As much data as possible (acq time)
  Voxel size compromise with resolution
  Postprocessing denoising
Minimize distortions
  Eddy currents distortions
  B0 inhomogeneity distortions
  Gradient non-linearity distortions
Minimize artifacts
  Gradient directions check
  Fat suppression
  Motion correction
  Partial volume: Isotropic voxels, whole-brain
  Cardiac gating
  Gibbs ringing
Diffusion sensitivity, speed, SNR
no distortions,
no artifacts
Impossible to optimize everything
General guidelines
Optimization details depend on goals
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion MRI: Acquisition factors

## Slide 55
Lecture 3 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain diffusion:
Why do we care?
How do we measure it?
How do we pre-process data?
Extracting information: models & challenges

## Slide 56
λ1/ε1
λ2/ε2
λ3/ε3
DT has 3 positive eigenvalues: λ1 λ2 λ3 → define the form of DT
DT has 3 orthogonal eigenvectors: ε1 ε2 ε3 → define the orientation of DT
A simple way of describing the directional dependence of diffusion is by using a diffusion tensor (DT)
A DT is 3x3 symmetric, positive-definite matrix
Basser et al. 1994
Planar anisotropy
Axial anisotropy
λ1 = λ2 = λ3
λ1 >> λ2 ~ λ3
λ1 = λ2 >> λ3
Isotropy
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion tensor model
Notes: How do we reperesent and visualize diffusion at each voxel in the brain?

## Slide 57
Fractional Anisotropy (FA)
Mean Diffusivity (MD)
l1+ l2 + l3
3
l1
l2
l3
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion tensor: microstructure estimates

## Slide 58
AD(x,y,z) = 1(x,y,z)
Largest eigenvalue
Axial diffusivity (AD)
RD(x,y,z) = [2(x,y,z) + 3(x,y,z)]/2
Average of two lower eigenvalues
Radial diffusivity (RD)
l1
l2
l3
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion tensor: microstructure estimates

## Slide 59
Challenge interpreting diffusion tensor results
Different biological processes may give similar estimations
Lack of specificity in terms of microstructure interpretation
FA in group 1
FA reduction in group 2
Decrease in
axon coherence?
Decrease in
myelin?
Both?
DTI white matter changes are not specific to the candidate cellular and molecular mechanisms driving the changes
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion tensor: model limitations

## Slide 60
Errors in areas with fiber crossing
DellAcqua Flavio, HBM 2015
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion tensor: microstructure estimates

## Slide 61
Areas with strong fiber crossing: wrong scalar estimations
Low fractional anisotropy (FA)
DellAcqua Flavio, HBM 2015
Jorge Jovicich
CIMeC, University of Trento, Italy
Diffusion tensor: microstructure estimates

## Slide 62
NODDI (multishell):
Estimates the orientation and dispersion of axons
FA OD Vic Viso
Steven et al. 2014
Zhang et al. 2012
Assaf et al. 2008
Diffusion Kurtosis Imaging (multishell):
Estimates the non-Gaussianity of the voxel
4th order tensor!
AxCaliber (multishell):
Measures axon diameter distribution
OD: orientation dispersion
VIC: volume fraction of intracellular compartment
VISO: volume fraction of isotropic CSF
Spherical Deconvolution (single and multishell):
Voxel signal response decomposed by stick responses with a fiber Orientation Densitity Function (fODF)
Jorge Jovicich
CIMeC, University of Trento, Italy
Beyond the diffusion tensor

## Slide 63
Diffusion MRI: Tractography
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 64
Concept map for lectures
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 65
Outline of tractography concepts
Jorge Jovicich
CIMeC, University of Trento, Italy
Tractography variables
Streamlines, seeds, step-size, interpolation
Starting and stopping criteria
Algorithm: deterministic vs. Probabilistic
Tractography quantification
Voxel-wise track counts (Track Density Imaging)
Structural connection strength
Both have issues:
  Biases to longer tracks
  Biases to simpler tracks
  Errors from noise & modelling

## Slide 66
Brain diffusion MRI challenges
Jorge Jovicich
CIMeC, University of Trento, Italy
Validation
Ex-vivo brain (hystology, dissection, axial tracings)
Phantom (digial, physical)
Quantification
What is connection strength? (#, volume of streamlines)
Integrated data from multiple modalities (T1, FA, myelin, etc)
Evaluation of quantitative maps along tracts
Promises: use morphology to estimate topology
Poupon et al., 2010

## Slide 67
Literature recommendations include
Jorge Jovicich
CIMeC, University of Trento, Italy
Web materials:
OHBM Educacional Series: https://www.pathlms.com/ohbm/courses/
https://www.ohbmbrainmappingblog.com/blog/ohbm-ondemand-how-to-diffusion-mri
ISMRM Educational Series
  https://www.ismrm.org/online-education-program/diffusion-perfusion-fmri-videos/
  https://www.youtube.com/watch?v=yluL093GMMA
  ...
Papers
Tournier. Diffusion MRI in the brain - Theory and concepts. Prog Nucl Magn Reson Spectrosc. 2019;112-113:1-16
Maier-Han et al., The challenge of mapping the human connectome based on diffusion tractography. Nat Comm. 2017;8(1):1349.
Jeurissen et al., Diffusion MRI fiber tractography of the brain. NMR Biomed. 2019;32(4):e3785
Le Bihan D, Iima M. Diffusion MRI: What Water Tells Us about Biological Tissues. PLoS Biol. 2015 Jul 23;13(7):e1002203
Microstructural imaging
...
http://www.ncbi.nlm.nih.gov/pmc/?term=diffusion+mri+review
.

## Slide 68
MR Image & Contrast
NMR Signal origin
Spatial encoding
Magnetic gradients
Pulse sequences
Powerful magnet
Radio frequency
Magnetic field gradients
MR Safety
Powerful magnet
Radio frequency
Magnetic field gradients
Structural MRI
Functional MRI
Diffusion MRI
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Pre-processing
Lecture 1
Lecture 2
Lecture 3
Lecture 4
Concept map for lectures
Jorge Jovicich
CIMeC, University of Trento, Italy