## Slide 1
Brain Functional MRI Introduction
Louvain-la-Neuve - Neuroimaging Workshop 2019
Jorge Jovicich
Center for Mind/Brain Sciences (CIMeC),
University of Trento, Rovereto, Italy
CIMeC: https://www.cimec.unitn.it/
MRI Lab: http://r.unitn.it/en/cimec/mri
E-mail: jorge.jovicich@unitn.it

## Slide 2
Functional MRI: Why?
Jorge Jovicich
CIMeC, University of Trento, Italy
Statistical Map
superimposed on anatomical MRI image
Functional images
Time
Condition 1
Condition 2
...
~ 5 min
Time
fMRI signal changes
In area of interest
Condition
~2s
Brain region
of interest
Source: Modified from Jody Culham’s fMRI Newbies web site
For example:
Condition 1: static dots
Condition 2: moving dots

## Slide 3
Lecture 4 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain functional MRI:
We want functional contrast:
  Blood Oxygenation Level Dependent (BOLD)
We want to measure signal fluctuations
  Fast MRI: Echo Planar Imaging
We want “clean” data for modeling & analysis
  Pre-processing

## Slide 4
Options:
Invasive
  Vascular volume (gadolinium)
Non-invasive
  Blood Oxygenation Level Dependent (BOLD)
  Perfusion (CBF: cerebral blood flow)
  CMRO2 (Cerebral metabolic rate O2 consumption)
  Vascular volume changes (VASO)
  … ongoing research (currents, diffusion, etc.)
standard
research
Brain Functional MRI Contrasts
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 5
BOLD contrast is the net result of two separate effects:
Hemodynamic response
Magnetic properties of the hemoglobin molecules
Blood Oxygenation Level Dependent (BOLD) contrast
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 6
Neural function relates to oxygen consumption
Inhaled air
  78% nitrogen
  21% oxygen
  1% inert gases (argon)
  0.04% carbon dioxide
Exhaled air
  78% nitrogen
  16% oxygen
  1% inert gases (argon)
  4% carbon dioxide
  Water vapour
C_6 H_12 O_6 + 6O_2
→ 6CO_2 + 6H_2 O + Energy released Glucose + Oxygen
→ Carbon dioxide + water + Energy
What happened?
Oxygen oxydized glucose to produce energy
Energy brain metabolism
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 7
Each red blood cell: about 250 million Hb molecules
Function: transport of ‘goods’ and ‘wastes’
  carries O2 to tissue and CO2 away from tissue
  one Hb molecule can carry up to 4 atoms of O2
Hemoglobin molecule structure:
four protein globin chains
each globin chain contains a heme group
at center of each heme group is an iron atom (Fe)
each heme group can attach an oxygen atom (O2)
Hemoglobin molecule states
  Oxy-hemoglogbin
  Deoxy-hemoglobin
Source: http://wsrv.clas.virginia.edu/~rjh9u/hemoglob.html,
Energy taxi: hemoglobin (Hb)
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 8
Source: Menon & Kim, TICS
Slide courtesy of Jody Culham
Brain weight: 2% of body weight
Brain energy budget: ~20% of body
Very efficient irrigation system
Brain vasculature & hemodynamic response
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 9
rCBF
dHg
rCBV
rCBV: regional Cerebral Blood Volume
rCBF: regional Cerebral Blood Flow
dHg: deoxygenated Hemoglobin
Hg: oxygenated Hemoglobin
Capillary during
baseline
Capillary during
activation
neuron
O2
Brain hemodynamic response
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 10
BOLD contrast is the net result of two separate effects:
Hemodynamic response
  Concentration of oxygenated hemoglobin changes with neural activation
  Changes are «local» to brain activation areas
  There is a quick decreas in oxy-Hg shortly after activation starts
  After a few seconds a local excess of oxy-Hg in active area is observed
Magnetic properties of the hemoglobin molecules
Blood Oxygenation Level Dependent (BOLD) contrast
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 11
Oxygenation states give rise to different magnetic states
  Oxygenated-Hb
    Isomagnetic with respect to the surrounding tissue, no net magnetization, paired electrons
  Deoxygenated-Hb
    Paramagnetic with respect to the surrounding tissue, net magnetization, unpaired electrons
  Pauling & Coryell, PNAS 1936.
Oxygenated Hg
Deoxygenated Hg
Full taxi
No passengers
Blood test tube inside an external magnetic field B0
Magnetic properties of hemoglobin (Hb)
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 12
De-oxygenation: shorter T2
Thulborn et al., 1982
T1: no effects
T2: clear effects
Hemoglobin oxygenation and the MRI signal
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 13
Gradient Echo
T2* changes
Test tubes, Ogawa 1990b
Oxyhemoglobin
Spin Echo
T2 changes
Deoxyhemoglobin
Little
difference
Large
difference
With fast T2*-weighted
image, we can measure
oxygenation changes
in blood!
Maybe we can use
blood oxygenation
changes specific
to brain function?
Hemoglobin oxygenation and the MRI signal
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 14
MR signal (Mxy)
Activation (more O2, less dHg, longer T2*)
Rest (more dHg, shorter T2*)
TE
t
S(TE) = S0 e–TE R2*
BOLD sensitivity: T2* and TE
Jorge Jovicich
CIMeC, University of Trento, Italy
Signal (t) = Mxy (t) = Mxy0 exp-TE/T2*

## Slide 15
Courtesy of P. Bandettini
Gray matter T2* changes
are relatively small
between activation
states.
The difference in T2*
shows an optimum
TE choice for the
maximum sensitivity
to detect changes of T2*
BOLD sensitivity: T2* and TE
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 16
TE (ms)
S(activation) – Signal(rest)
TEoptimum  T2* (active_tissue)
Optimal
range
BOLD sensitivity: T2* and TE
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 17
Baseline
Rise
Rise
Peak
Peak
Undershoot
Undershoot
Sustained Response
Initial Dip
Initial Dip
Block
design
Single-event
design
t (seconds after stimulation)
Response to
a series of
brief stimulus
Response to
one brief
stimulus
~5s
~12s
~2s
Courtesy of Allen Song
If [dHb]  MR signal
If [dHb]  MR signal 
MRI measure of the hemodynamic response
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 18
Brain activity responses to whisker
stimulation in mice with contrast agent
From Huettel, Song and McCarthy
BOLD specificity: suboptimal
Jorge Jovicich
CIMeC, University of Trento, Italy
  deoxy-Hb can change because:
      Metabolism to support neuronal activation
    Blood flow changes
    Blood volume changes
  BOLD measures the combined effect
CBF: Cerebral Blood Flow
CBV: Cerebral Blood Volume
BOLD: Blood Oxygenation Level Dependent

## Slide 19
Evidence that BOLD response reflects pooled local field potential activity (Logothetis 2001)
BOLD specificity: there is hope
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 20
Lecture 4 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain functional MRI:
We want functional contrast:
  Blood Oxygenation Level Dependent (BOLD)
We want to measure signal fluctuations
  Fast MRI: Echo Planar Imaging
We want “clean” data for modeling & analysis
  Pre-processing

## Slide 21
High Functional sensitivity
  T2* gives the strongest BOLD effects
High Speed
  Fast acquisition to follow signal dynamics
High Spatial resolution
  To understand anatomical location of activity
High Functional specificity
  To correctly interpret signal fluctuations
What sequence would we like for fMRI?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 22
EPI: standard imaging sequence for fast MRI
(brain fMRI, diffusion, perfusion, etc.)
EPI advantages for brain fMRI
  Nowadays easily available
  Dominant contrast is T2* (BOLD)
    Spin-echo EPI can have T2 & T2*
  Typically allows full brain coverage in 1sec (or less!)
  with 2 mm isotropic voxels (or less!)
EPI limitations:
  High sensitivity to local magnetic field inhomogeneities
    - Signal loss and image distortions
  Gradient switching: Nyquist ghost
  Loud
  Signal decay during acquisition limits spatial resolution
Echo Planar Imaging (EPI)
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 23
S(t)
“slice select”
“freq. enc”
(read-out)
RF
t
Gz
Gy
Gx
kx
ky
Conventional MRI
(gradient-echo)
one RF excitation,
one line of kspace...
TE
Structural versus EPI MRI
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 24
S(t)
“slice select”
“freq. enc”
(read-out)
RF
t
Gz
Gy
Gx
kx
ky
RF
t
S(t)
t
Gz
Gy
Gx
etc...
T2*
Conventional MRI
(gradient-echo)
kx
ky
Echo-planar imaging
(gradient-echo)
one RF excitation,
one line of kspace...
one RF excitation,
many lines of k-space...
What sequence would we like for fMRI?
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 25
S(TE) = S0 e–TE/T2*
Gradient-echo EPI (T2*)
Spin-echo EPI (T2 and T2*)
K-space trayectory
Standard EPI
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 26
Structural MRI (T1-weighted)
1x1x1 mm3, 328 s
Functional MRI (T2*-weighted)
2x2x2 mm3, 1 s
3T Prisma Siemens, 64 head/neck channel coil
Example
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 27
Lecture 4 outline
Jorge Jovicich
CIMeC, University of Trento, Italy
Brain functional MRI:
We want functional contrast:
  Blood Oxygenation Level Dependent (BOLD)
We want to measure signal fluctuations
  Fast MRI: Echo Planar Imaging
We want “clean” data for modeling & analysis
  Pre-processing

## Slide 28
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing
Normalization

## Slide 29
Look for problems, for example:
Dental artifact
RF interference
Metalic hair pin
Severe motion
Severe signal
inhomogeneity
Poor contrast
Wrap around
Lesion
Jorge Jovicich
CIMeC, University of Trento, Italy
LOOK at the data DURING the experiment

## Slide 30
And look for problems, for example:
Signal loss
Fat signal
Hardware problems
Distortions
Jorge Jovicich
Jorge Jovicich
CIMeC, University of Trento, Italy
LOOK at the data DURING the experiment

## Slide 31
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing
Normalization

## Slide 32
The problem:
  Image reconstruction assumes uniform B0 in the sample
  In reality this is not true:
  As a result, EPI shows:
    areas with signal loss (where T2*<<TE): nothing to do!
    areas with geometric distortions: something to do!
x, y : amounts of shift (misplacement) in x, y directions in mm
FOVx, FOVy : field of view in x, y direction in mm
tx, ty : sampling interval in x, y direction ( 1/sampling rate)
Voxel shifts relative to
true voxel location.
So:
If B is measured
we can shift back voxel
Jorge Jovicich
CIMeC, University of Trento, Italy
Geometric distortions in EPI

## Slide 33
Significance
- Misregistration of EPI and Anatomical image
 Incorrect mapping of region of interest(ROI)
 Need to be corrected using Fieldmap
Distorted
EPI
Undistorted
structural
Field
map
Jorge Jovicich
CIMeC, University of Trento, Italy
Geometric distortions in EPI

## Slide 34
Ventral/amygdala
Frontal
~ 2 mm distortions close to the amygdala
11 mm distortions at the ventricles
14 mm distortions ant grey matter
Small residual field map errors
Jorge Jovicich
CIMeC, University of Trento, Italy
EPI geometric distortions and correction

## Slide 35
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing
Normalization

## Slide 36
Modified from Source: Huettel S.A., Song A.W., McCarthy G.
Motion (even 1 voxel) = Large artificial ‘brain activation’
Jorge Jovicich
CIMeC, University of Trento, Italy
Head motion effects

## Slide 37
Define a reference image from the EPI time series
Iteratively co-register (minimize a cost function) each EPI to reference
  Determine the rigid body transformation that minimizes
  For each corrected EPI the transformation is defined by
  3 translations - in X, Y & Z directions.
  3 rotations - about X, Y & Z axes.
Jorge Jovicich
CIMeC, University of Trento, Italy
Motion correction: co-registration to reference

## Slide 38
Could be acceptable motion
Too much motion (>> 1mm)
Modified from Source: Huettel S.A., Song A.W., McCarthy G.
Jorge Jovicich
CIMeC, University of Trento, Italy
Motion correction results

## Slide 39
Modified from Source: Huettel S.A., Song A.W., McCarthy G.
Jorge Jovicich
CIMeC, University of Trento, Italy
Motor fMRI without/with motion correction
Corrected
Uncorrected

## Slide 40
Head Vise
(more comfortable than it sounds!)
Bite Bar
Often collaboration and foam padding works as well as anything
Vacuum Pack
Thermoplastic mask
Source: modified from Jody Culham
Jorge Jovicich
CIMeC, University of Trento, Italy
Reducing head motion
Notes: 40

## Slide 41
Tell your subjects how to be good subjects
  “Don’t move” is too vague
Make sure the subject is comfy going in
  avoid “princess and the pea” phenomenon
Emphasize importance of not moving at all during beeping
  do not change posture
  if possible, do not swallow
  do not change posture
  do not change mouth position
  do not tense up at start of scan
Discourage any movements that would displace the head between scans
Do not use compressible head support
Example of info for first-time subjects:
  http://defiant.ssc.uwo.ca/Jody_web/Subject_Info/firsttime_subjects.htm
Source: Jody Culham
Jorge Jovicich
CIMeC, University of Trento, Italy
Reducing motion: Prevention best remedy

## Slide 42
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing
Normalization

## Slide 43
The problem:
  Ideally
    Each brain volume is acquired instantaneously
    Each volume time point represents the cognitve
    state of the whole brain related to that time point
  In reality
    Echo image slice is acquired at a different time
      Sequential slice acquisition
      Interleaved slice acquisition
  Consequence:
    inacurrate representation of hemodynamic response
Solutions:
  Reduce the time for whole-brain sampling
  Postprocessing: temporal interpolation
Jorge Jovicich
CIMeC, University of Trento, Italy
Slice acquisition timing correction

## Slide 44
The problem
Modified from Source: Huettel S.A., Song A.W., McCarthy G.
Interleaved Acquisition
Slice 15, Slice 17, …, Slice 16
Ideal hemodynamic
response for the active
area: same for all slices
Time errors: different
responses for different slices.
Jorge Jovicich
CIMeC, University of Trento, Italy
Slice acquisition timing correction

## Slide 45
Estimate for each voxel, the signal intensity that would have corresponded to a time shift that aligns all slices to a reference acquisition time.
SEQUENTIAL slice acquisition: functional volume are shifted in time
This is corrected by sinc (or linear) interpolation in time
Jorge Jovicich
CIMeC, University of Trento, Italy
Slice acquisition timing correction

## Slide 46
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Normalization
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing

## Slide 47
Single subject or group analyses:
  For each subject:
    Co-registration between fMRI and anatomical scans
      Rigid body transformation (cost function minimized)
      This adds an interpolation step (smoothing)
    Co-registration (normalization) of both (now aligned) to standard atlas
      For spatial reference
      Talairach space, or probabilistic atlases, cortical surface based
      This adds an interpolation step (smoothing)
      Caveats: normalization space may not represent all subjects
EPI
Anatomical
Standard Template
Co-registration
Normalization
Jorge Jovicich
CIMeC, University of Trento, Italy
Co-registrations and Normalization

## Slide 48
Talairach space (proportional grid system)
  From atlas of Talairach and Tournoux (1988)
  Based on single subject (60y, Female, Cadaver)
  Single hemisphere
  Related to Brodmann coordinates
Montreal Neurological Institute (MNI) space
  Combination of many MRI scans on normal controls
    All right-handed subjects
  Approximated to Talaraich space
    Slightly larger
    Taller from AC to top by 5mm; deeper from AC to bottom by 10mm
  Used by SPM, National fMRI Database, International Consortium for Brain Mapping
Jorge Jovicich
CIMeC, University of Trento, Italy
Standardized spaces (brain atlas)

## Slide 49
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Normalization
Slice timing
correction
Spatial smoothing
Quality
check
Signal
model
etc.
Temporal smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing

## Slide 50
Goal: remove fluctuations that may be attributed to sources of no interest
Identify unwanted frequency variation
  Drift (low-frequency)
  Physiology: cardiac (1-1.5 Hz), respiratory (0.2-0.3 Hz)
  Task overlap (high-frequency)
Reduce power around those frequencies through application of filters
Potential problem: removal of frequencies composing response of interest
Jorge Jovicich,
Jorge Jovicich
CIMeC, University of Trento, Italy
Temporal filtering fMRI data

## Slide 51
Source: Smith chapter in Functional MRI:
An Introduction to Methods
Huettel, Song & McCarthy, 2004,
Functional Magnetic Resonance Imaging
Signal drifts from
hardware instabilities
Drift on an activation
time course
Jorge Jovicich
CIMeC, University of Trento, Italy
Temporal filtering fMRI data
Notes: 51

## Slide 52
Respiration
Every 4-10 sec (0.3 Hz)
Moving chest distorts susceptibility
Cardiac Cycle
Every ~1 sec (0.9 Hz)
Pulsing motion, blood changes
Solutions
Gating
Filter AND avoiding paradigms at those frequencies
You want your paradigm frequency to be in a “sweet spot” away from the noise
Source: Jody Culham
http://www.fil.ion.ucl.ac.uk/spm/course/
Signal fluctuations due to respiration
Jorge Jovicich
CIMeC, University of Trento, Italy
Temporal filtering fMRI data
Notes: 52

## Slide 53
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing
Normalization

## Slide 54
Spatial smoothing essentially ‘blurs’ your functional data.
Why would you ever want to reduce the spatial resolution of your data?
Spatial smoothing may often be required when averaging data across several subjects due to the individual variations in brain anatomy and functional organization.
Increased degrees of smoothing (FWHM)
Gaussian smoothing kernel
Jorge Jovicich
CIMeC, University of Trento, Italy
Spatial smoothing

## Slide 55
Unsmoothed Data
Smoothed Data (kernel width 5 voxels)
Modified from Source: Huettel S.A., Song A.W., McCarthy G.
Jorge Jovicich
CIMeC, University of Trento, Italy
Spatial smoothing: reducing false positives

## Slide 56
Modified from Source: Huettel S.A., Song A.W., McCarthy G.
Jorge Jovicich
CIMeC, University of Trento, Italy
Spatial smoothing: reducing false positives

## Slide 57
Advantages
  Increases Signal to Noise Ratio (SNR)
    Matched Filter Theorem: Maximum increase in SNR by filter with same shape/size as signal
  Reduces number of comparisons
    Allows application of Gaussian Field Theory
  May improve comparisons across subjects
    Signal may be spread widely across cortex, due to intersubject variability
Disadvantages
  Reduces spatial resolution
  Challenging to smooth accurately if size/shape of signal is not known
  Notes:
  Often used in general linear model analysis
  Often not used in layer fMRI
Jorge Jovicich
Spatial smoothing

## Slide 58
dMRI
dicom
fMRI nii
sMRI nii
Distortion Correction
Head motion correction
Slice timing
correction
Temporal smoothing
Quality
check
Signal
model
etc.
Spatial smoothing
Various pre-processing tools available:
https://www.fil.ion.ucl.ac.uk/spm/
https://fsl.fmrib.ox.ac.uk/fsl
https://afni.nimh.nih.gov/
...
This is a generic example
Jury out for optimal details
Sample preparation
Pre-processing: analyses steps to minimize noise, artifacts to get the «cleanest» data for models
Acquisition
Jorge Jovicich
CIMeC, University of Trento, Italy
fMRI MRI pre-processing
Normalization

## Slide 59
Literature recommendations include
Jorge Jovicich
CIMeC, University of Trento, Italy
Collection of overview papers from various leaders in the field
20 years of fMRI
Reproducibility in Neuroimaging
MRI of cortical layers
Cleaning up fMRI time series
Web materials:
https://practicalfmri.blogspot.com/
http://www.fmri4newbies.com/
OHBM Educacional Series: https://www.pathlms.com/ohbm/courses/ (tons of stuff!)
ISMRM Educational Series: https://www.ismrm.org/education/
  https://www.ismrm.org/online-education-program/diffusion-perfusion-fmri-videos/
https://gate.nmr.mgh.harvard.edu/wiki/whynhow/
.

## Slide 60
MR Image & Contrast
NMR Signal origin
Spatial encoding
Magnetic gradients
Pulse sequences
Powerful magnet
Radio frequency
Magnetic field gradients
MR Safety
Powerful magnet
Radio frequency
Magnetic field gradients
Structural MRI
Functional MRI
Diffusion MRI
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Analyses & applications
Contrast, important parameters
Sequences & artifacts
Pre-processing
Lecture 1
Lecture 2
Lecture 3
Lecture 4
Concept map for lectures
Jorge Jovicich
CIMeC, University of Trento, Italy

## Slide 61
Acknowledgements
http://r.unitn.it/en/cimec/mri
Giovanni
Frisoni
Moira
Marizzoni
L. Novello
C. Maffei
D. Zacà
Silvio
Sarubbo
F. Saviola
Valeria d.
Maggiore
Flor
Jacobacci
Olivier
Collignon
M. Akinci
V. Iacovella
S. Tambalo
Collaborators
include
Current /recent lab include
N. Pace

## Slide 62
Tonight (http://www.milonga.be)
TANGO BAR
21:30 - 02:00
Rue de Dublin 13, 1050 Ixelles, Belgium MILONGA BRUSSELS